## Slide 1: Ideal User Workflow
User Goal
        Input
          Energy Start, (Energy End,) Polarisation Start, (Polarisation End,) Steps, Polarisation Mode, (Raster/Direct, Harmonic)
        Output
          Data correlating Energy and Polarisation to Sensor Readout.
            Pretty Graphics…
            Peak fitting…
            Analysis

## Slide 2: Invisible Workflow
User Goal
        Input
          Energy Start, (Energy End,) Polarisation Start, (Polarisation End,) Steps, Polarisation Type, (Raster/Direct, Harmonic)
        Undulator Trajectory and Monochromator Trajectory
        Other control magics (data collection triggers etc).
        Output
          Data correlating Energy and Polarisation to Sensor Readout.
            Data analysis workflows, jiggery pokery
            Pretty Graphics…
            Peak fitting…
            Analysis

## Slide 3: Undulator Tables
User Goal
        Input
          Energy Start, (Energy End,) Polarisation Start, (Polarisation End,) Steps, Polarisation Type, (Raster/Direct, Harmonic)
        Undulator Trajectory and Monochromator Trajectory
        Other control magics (data collection triggers etc).
        Output
          Data correlating Energy and Polarisation to Sensor Readout.
            Data analysis workflows, jiggery pokery
            Pretty Graphics…
            Peak fitting…
            Prompt Analysis

## Slide 4: Undulator Tables
Present Situation
        1-D Undulator Tables allowing fixed POLARISATION or fixed ENERGY
        Requires new tables to be loaded for each use case (although most common use cases are fixed horizontal or vertical polarisation)
          does not allow for input of the form
          Energy Start, (Energy End,) Polarisation Start, (Polarisation End,) Polarisation Type, (Raster/Direct, Harmonic)
Desired Situation
        A single table for all seasons that can be used to calculate all undulator trajectories
  Implications…
    We have 5 dimensions of data required, with 4 parameters needed to calculate the final variable pair
        Each parameter (Energy, Polarisation, Polarisation Mode, Harmonic) maps to a 1-D variable (Gap, Shift)
        Produce 5D data
        Or 3 dimensions of 2D text tables… somehow.

## Slide 5: Code/Script – ‘Ephitogapshift’
Object Oriented Python Script
  Key Classes & Methods
Undulator Motion
GapShiftEnergyPoln
__init__
__init__
create_motion_trajectory
check_valid_motion
save_motion_txt
save_lookup_json
save_lookup_h5
create_inverse_lookups
save_lookup_txt
save_lookup_pickle

## Slide 6: Meat of Script – GapShiftEnergyPoln class
Purpose of class
        To create an inverse lookup table based on a pre-calculated table of Gap/Shift/Energy/Polarisation/Harmonic/Polarisation Mode.
        Loads a table calculated from a Radia model, stored as an ASCII text file (at the moment)
  Methods
      __init__(self, pre-calculated gap-shift table)
        instantiates the class with an attribute containing the table from the pre-calculated gap-shift table.
      create_inverse_lookup(self)
        uses the matplotlib.tri library to interpolate the gap-shift table and create a reverse lookup function.
          very iffy at the low gap boundary
  Notable Attributes
      gapshifttable
        A numpy array holding information from the precalculated Radia model
      inverse_lookup
        Dict of 2N elements, where N is the number of harmonics available in the gapshifttable
          Dict names as [‘{} Gap’.format(harmonic)]; [‘{} Shift’.format(harmonic)],
            where harmonic is ‘Harmonic 1’, ‘Harmonic 3’, ‘Harmonic 5’,…
          Each dict element contains inverse lookup method, that are CubicTriInterpolator from matplotlib.tri

## Slide 7: Bookkeeping element of script – UndulatorMotion
Purpose of Class
        Create final trajectories for move requests.
        Save as text (or other format) file outputs
      Create_Motion_Trajectory(Scientist input parameters for energy, polarisation, steps etc)
        Simply creates the first 4-D of the 5-D table (i.e. the parameters for the inverse_lookup function)
          energy, polarisation, mode, harmonic values
      check_valid_motion(self)
        Calls the GSEP.inverse_lookup function to calculate the gap/shift values of the trajectory for all requested harmonics
          GSEP.inverse_lookup returns NaN for unavailable interpolations.
          check_valid_motion excludes any motion containing unavailable positions
        Saves a list of allowed harmonics for the complete move
        Saves the trajectories to the motion attribute
      save_motion_txt(self)
        Creates a separate tab separated text file with four columns for each allowed harmonic trajectory
          Energy Polarisation Gap Shift
          Harmonic is given in file name

## Slide 8: Saving Out Lookup Tables– UndulatorMotion
Purpose of Class
        Functions to save data as table or dict to various file formats
Save Functions
        save_lookup_txt
        save_lookup_json
        save_lookup_pickle
        save_lookup_h5

## Slide 9: Potential File Formats – ASCII Text 1701 x 37 = 62937 elements
ASCII Table Formats
      .icv.txt
        Because we are dealing with 5/6 dimensional arrays, 2D table files Just Don’t Work
        Tables must be reconstituted to original dimensions to be addressed
          Held in a comment line
        .icv.txt file (“I Choose Violence” text file)
          flattened 6D table that includes axis values. (VERY LARGE file)
          1.9 Million lines
          44 Mb
          Direct editing practically impossible

## Slide 10: Potential File Formats – JSON 1701 x 37 = 62937 elements
list.json
        (Numpy) arrays are not json serialisable, so must be converted to either a list or a dict
  List.json
          must be reconverted to an arrays to be sensibly addressed
          All data is there, including column headers.
          Table Shape is retained
          5M lines
          48 Mb
          Metadata needed in comment lines
          Direct editing practically impossible
  Dict.json
        Dict can be directly addressed once loaded
          755 thousand lines
          10 Mb
          Metadata possibly included in dict structure
          direct editing difficult – locating edit point

## Slide 11: Potential File Formats – Pickle 1701 x 37 = 62937 elements
table.pkl
        (Numpy) arrays can be pickled
          binary format, can be reloaded into python quickly
  Table.pkl
        must be unpickled
        Metadata not in direct table
        14Mb
        Not human readable
          utter gibberish
          impossible to directly edit
  Dict.pkl
        Must be unpickled
        Dict can be directly addressed once loaded
          11 MbMetadata possibly included in dict structure
        Not human readable
          utter gibberish
          impossible to directly edit

## Slide 12: Potential File Formats – hdf5 1701 x 37 = 62937 elements
.h5
        Not really ‘table vs dict’
        it’s own format
          binary format, can be reloaded into python quickly
  Axes
        Axis information stored separately and ‘attached’ to array axes in object-oriented manner
          range, units, label
        Metadata tightly bound to data
  Data
        With appropriate viewer
          e.g. DataVis in DAWN
        (Numpy) array can be saved
  .h5
        Not human readable with text editor

## Slide 13: Potential File Formats – hdf5 1701 x 37 = 62937 elements
But with the right viewer/editor
  DataVis in DAWN
        Axis information viewable as table or plot

## Slide 14: Potential File Formats – hdf5 1701 x 37 = 62937 elements
But with the right viewer/editor
  DataVis in DAWN
        Data viewable as table or surface plot

## Slide 15: Next Steps
User Tuning
        Figure out a way of sensibly correcting the tables using User Data
          Interpolating to user data risks fitting to noise
          Directly calculated data has the right surface shape, but is often in the wrong position
            Apertures, electron beam position, magnetic measurement errors &c
  Requirement
        Fitting surface to data…
          Apply an Nth order 2D polynomial fit to the differences between measured and calculated values.
          Subtract fitted ‘difference surface’ to calculated data.